## Slide 1
Presented to CASA systems | DD - MMM - YYYY
Alepo 5G Troubleshooting

## Slide 2: AGENDA

## Slide 3: Agenda
Alepo PCF Troubleshooting
Alepo SDM Troubleshooting Manual

## Slide 4: Alepo PCF Troubleshooting

## Slide 5: Alepo PCF Troubleshooting
This troubleshooting section describes how to identify the cause of failures in the PCF and how to troubleshoot them.
This troubleshooting procedures is intended for the PCF module of Alepo 5G solution ACC 21.2.1.
Alepo PCF includes the following components:
  UDR
  PCF-PCRF
  PCF Portal

## Slide 6: Alepo PCF Troubleshooting
This chapter describes the major PCF issues a subscriber might encounter in 4G and 5G networks.
AM Policy is not getting applied to subscriber
SM Session Policy is not getting applied to subscriber
SM Session Policy is applied to subscriber but not getting desired QoS
SM Session Policy is applied to subscriber, but usage monitoring is not enabled
SM Authorization Policy is not getting applied to subscriber
Access Network Information is not received at AF
P-CSCF Restoration is not successful

## Slide 7: AM Policy is not getting applied to subscriber

## Slide 8: AM Policy is not getting applied to subscriber
Possible Causes
AM policy allocation can fail due to the following reasons:
  Requested SUPI is not present in the system
  User has not subscribed to AM policy
  AM policy evaluation failure
  UDR PCF is not reachable
Preprocessing
Check if the UDR and UDRPCF are up and running.
Check if a fault alarm is generated by any of the network functions.

## Slide 9: AM Policy is not getting applied to subscriber
Troubleshooting Procedure
The following section includes troubleshooting steps for various API messages and their error codes:
HTTP Error Code 400
This API message and error code can occur due to multiple reasons:
Case 1
Message - API : AM Policy Associations (Create)
Reason :
Unknown SUPI
SUPI is not present in UDR
The end-user specified in the request is unknown to the PCF

## Slide 10: AM Policy is not getting applied to subscriber
Steps to Resolve:
Check if the subscriber is present in the SDM portal by searching it through the Subscriber Management menu in the SDM portal.
2. If Subscriber is not present, then provision the subscriber via SIM Batch Management & Subscriber Management menus in SDM portal.
3. If the subscriber is present, check if the policy is associated with the subscriber by clicking the View Subscriber option:
4. Select Policy dropdown in the Data Type section and check for AM Policy Section.
5. If no category is associated with a subscriber under AM Policy Tab, then assign a subscriber category. This will complete AM policy association.
Check Logs

## Slide 11: AM Policy is not getting applied to subscriber
Case 2
Message: API - AM Policy Associations (Create)
Reason: AM policy evaluation failure (Matching AM policy not found)
Steps to Resolve:
Check for Subscriber category by searching and viewing subscriber in Subscriber Management -> Policy dropdown in Data Type.
2. Obtain subscriber category from step 1 and search this category in PCF portal under Subscriber Categories.
3. Once you find a category, check AM Policy section in the category. Then check rules configured to evaluate a particular AM policy.
4. If the rules do not have the correct configuration, then correct it as per business needs by using various condition assets.
Check Logs

## Slide 12: AM Policy is not getting applied to subscriber
Case 3
Message: API: Individual AM Policy Association (Update)
Reason: AM policy association is not present in PCF. The end-user specified in the request is unknown to the PCF.
Resolution:
Ensure AM policy association is present and re-create AM policy session from AMF. This is a client-side error from AMF.
Check Logs

## Slide 13: AM Policy is not getting applied to subscriber
Case 4
Message: API - Individual AM Policy Association (Update)
Reason: AM policy evaluation failure (Matching AM policy not found.)
Steps to resolve:
Check subscriber category by searching and viewing subscriber in Subscriber Management -> Policy dropdown in Data Type.
2. Obtain subscriber category from step 1 and search this category in PCF portal under Subscriber Categories
3. Once you find a category, check AM P olicy section in the category. Check for rules configured under this section to evaluate a particular AM policy.
4. If the rules do not have the correct configuration, then correct it as per business needs and use various condition assets.
Check Logs

## Slide 14: AM Policy is not getting applied to subscriber
HTTP Error Code 500
Message: API - AM Policy Associations (Create) / Individual AM Policy Association (Update)
Reason: UDR PCF is not reachable (UDR service down)
Steps to resolve:
Check if the UDRPCF is running. The process of checking depends on the type of infrastructure. In the case of Kubernetes, there must be a container within pcf-pcrf pod (or UDRPCF can be deployed as a separate standalone pod).
2. If it is not running, then start the process of checking UDRPCF. In the case of Kubernetes, UDRPCF gets auto restarted after 40 seconds.
Check Logs

## Slide 15: SM Session Policy is not getting applied to subscriber

## Slide 16: SM Session Policy is not getting applied to subscriber
Possible Causes
  Authentication of a subscriber can fail due to the following causes:
  Requested SUPI is not present in the system
  User has not subscribed to SM policy
  SM policy evaluation failure (PCC Rule or Session Rule)
  UDR PCF is not reachable
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 17: SM Session Policy is not getting applied to subscriber
Troubleshooting Procedure
The following section includes troubleshooting steps for various API messages and their error codes:
HTTP Error Code 400
This API message and error code can occur due to multiple reasons:
Case 1
Message - API: SM Policies (Create)
Reason:
Incorrect SUPI passed in request Body
End user specified in the request is unknown to the PCF
Steps to Resolve:
Check if the subscriber is present in the SDM portal by searching it through Subscriber Management menu in SDM portal.
If Subscriber is not present, then Provision subscriber via SIM Batch Management & Subscriber Management menus in SDM portal.
If subscriber is present, check if policy is associated with subscriber by clicking the View Subscriber, selecting Policy dropdown in Data Type section, and checking for Subscribed Slice section.
If subscriber is not associated to subscribed slice, then assign a slice to the subscriber from the same menu. Also, assign Usage Monitoring if necessary. This will complete SM policy association.
Check Logs

## Slide 18: SM Session Policy is not getting applied to subscriber
Case 2
Message: API: SM Policies (Create) / Individual SM Policy (Update)
Reason: All rules of SM Session failed. (No SM Session rules evaluated)
Steps to resolve:
Check Subscriber category by searching and viewing subscriber in Subscriber Management -> Policy dropdown in Data Type section check Subscriber Category.
Obtain subscriber category from step 1 and search this category in PCF portal under Subscriber Categories
Find category check SM P olicy section in the category for session or under PCC policy, check for rules configured to evaluate a particular SM policy.
If the rules do not have the correct configuration, then correct it according to your business needs and by using various condition assets.
Check Logs

## Slide 19: SM Session Policy is not getting applied to subscriber
Case 3
Message: API: Individual SM Policy (Update)
Reason:
SM policy association is not present in PCF
SM session record not found in database
Unknown smPolicyId is received
Steps to Resolve:
Ensure SM policy association is present
Re-create SM policy session from SMF
Check Logs

## Slide 20: SM Session Policy is applied to subscriber but not getting desired QoS

## Slide 21: SM Session Policy is applied to subscriber but not getting desired QoS
Possible Causes
The issue with desired QoS can occur due to the following reasons:
  If a static PCC rule is applied, then incorrect QoS is pre-defined against PCC rule in SMF/PGW.
  If a dynamic PCC rule is applied, then incorrect QoS is pre-defined against PCC rule in PCF.
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 22: SM Session Policy is applied to subscriber but not getting desired QoS
Troubleshooting Procedure
Steps to Resolve
If a static PCC rule is allocated, then validate pre-defined QoS or static PCC rule in SMF or PGW with the one configured in PCF.
If a dynamic PCC rule is allocated, then pre-defined QoS or dynamic PCC rule in PCF must be re-checked.
Do this from the PCF Portal under Policy Management -> SM Policies
Check if the evaluated rule is configured with a QoS information.
On SM policy update, if new policy with new desired QoS is expected, then validate the old PCC rule removal & new PCC rule installation in both SMF/PGW & PCF.
Check Logs

## Slide 23: SM Session Policy is applied to subscriber but not getting desired QoS
Troubleshooting Procedure
Steps to Resolve
If a static PCC rule is allocated, then validate pre-defined QoS or static PCC rule in SMF or PGW with the one configured in PCF.
If a dynamic PCC rule is allocated, then pre-defined QoS or dynamic PCC rule in PCF must be re-checked.
Do this from the PCF Portal under Policy Management -> SM Policies
Check if the evaluated rule is configured with a QoS information.
On SM policy update, if new policy with new desired QoS is expected, then validate the old PCC rule removal & new PCC rule installation in both SMF/PGW & PCF.
Check Logs

## Slide 24: SM Session Policy is applied to subscriber, but usage monitoring is not enabled

## Slide 25: SM Session Policy is applied to subscriber, but usage monitoring is not enabled
Possible Causes
Issue with enabling usage monitoring can be due to the following reasons:
  Usage monitoring limit ID is not associated with subscriber SM policy
  Usage monitoring limit ID is not associated with evaluated SM policy PCC rule
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 26: SM Session Policy is applied to subscriber, but usage monitoring is not enabled
Troubleshooting Procedure
In the case of Association with SM Policy
Steps to resolve
  Go to SDM portal and subscription management
  Search for relevant SUPI and view SM policy data
  Check if the usage limit is associated with SM policy. If not, then associate the required usage limit.
In the case of Association with SM policy PCC rule
Steps to Resolve
  Go to PCF portal and PCC rules
  Search for evaluated SM policy PCC rule name and view rule configuration
  Check if usage limit is associated with PCC rule, if not, then associate the required usage limit
Check Logs

## Slide 27: SM Session Policy is applied to subscriber, but usage monitoring is not enabled
Troubleshooting Procedure
In the case of Association with SM Policy
Steps to resolve
  Go to SDM portal and subscription management
  Search for relevant SUPI and view SM policy data
  Check if the usage limit is associated with SM policy. If not, then associate the required usage limit.
In the case of Association with SM policy PCC rule
Steps to Resolve
  Go to PCF portal and PCC rules
  Search for evaluated SM policy PCC rule name and view rule configuration
  Check if usage limit is associated with PCC rule, if not, then associate the required usage limit
Check Logs

## Slide 28: SM Authorization Policy is not getting applied to subscriber

## Slide 29: SM Authorization Policy is not getting applied to subscriber
Possible Causes
  SM Authorization Policy can fail due to the following reasons:
  Corresponding IP CAN session is not available on Npcf_SMPolicy Interface
  IP CAN session is online with emergency DNN
  PCF network function is not reachable
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 30: SM Authorization Policy is not getting applied to subscriber
Troubleshooting Procedure
The following section includes troubleshooting steps for various Rx Diameter supported messages and their result codes:
Diameter Result Code 5065
Message - Initial Provisioning of Session Information - Rx AAR
Diameter Error Message: PDU session record not found in database
Reason: The corresponding IP CAN session is not available on Npcf_SMPolicy Interface.
Steps to resolve:
Ensure that SM Session Policy session is available.
If unavailable, create new SM Session Policy session.
Check Logs

## Slide 31: SM Authorization Policy is not getting applied to subscriber
Troubleshooting Procedure
The following section includes troubleshooting steps for various Rx Diameter supported messages and their result codes:
Diameter Result Code 5065
Message - Initial Provisioning of Session Information - Rx AAR
Diameter Error Message: PDU session record not found in database
Reason: The corresponding IP CAN session is not available on Npcf_SMPolicy Interface.
Steps to resolve:
Ensure that SM Session Policy session is available.
If unavailable, create new SM Session Policy session.
Check Logs

## Slide 32: SM Authorization Policy is not getting applied to subscriber
Diameter Result Code 5066
Message - Initial Provisioning of Session Information - Rx AAR
Diameter Error Message: PDU session is not established to an Emergency DNN
Reason: IP CAN session is online with emergency DNN
Resolution:
Ensure that IP CAN session is available with non-emergency DNN.
Check Logs

## Slide 33: Access Network Information is not received at AF

## Slide 34: Access Network Information is not received at AF
Possible Causes
  ANI information retrieval can fail due to the following reasons:
  The corresponding IP CAN session is not available on Npcf_SMPolicy Interface
  PCF network function is not reachable
  Network Access feature is not supported at SMF
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 35: Access Network Information is not received at AF
Troubleshooting Procedure
The following section includes troubleshooting steps for various Rx Diameter supported messages and their result codes:
Diameter Result Code 2001 (With NetLoc-Access-Support)
Message - Reporting Access Network Information - Rx AAR
Diameter Error Message: None
Reason: Network Access Feature is not supported at SMF
Steps to resolve:
Ensure that SM Session Policy session is available with access network feature support.
If unavailable, create new SM Session Policy session.
3. Check Logs

## Slide 36: P-CSCF Restoration is not successful

## Slide 37: P-CSCF Restoration is not successful
Possible Causes
  P-CSCF Restoration can fail due to the following reasons:
  Corresponding IP CAN session is not available on Npcf_SMPolicy Interface
  PCF network function is not reachable
  P-CSCF Restoration Feature is not supported at SMF
  P-CSCF Restoration fails at SMF
Preprocessing
  Check if the UDR and UDRPCF are up and running.
  Check if a fault alarm is generated by any of the network functions.

## Slide 38: P-CSCF Restoration is not successful
Troubleshooting Procedure
The following section includes troubleshooting steps for various Rx Diameter supported messages and their result codes:
Diameter Result Code 5012
Case 1
Message : P-CSCF Restoration Enhancement Support - Rx AAR
Diameter Error Message: Feature not supported in SMF Supported Features
Reason: P-CSCF Restoration Feature is not supported at SMF
Steps to resolve:
Ensure that SM Session Policy session is available with P-CSCF restoration feature support.
If unavailable, create new SM Session Policy session.
Check Logs

## Slide 39: P-CSCF Restoration is not successful
Case 2
Message - P-CSCF Restoration Enhancement Support - Rx AAR
Diameter Error Message: Feature not supported in SMF Supported Features
Reason: P-CSCF Restoration fails at SMF
Steps to resolve:
Check on SMF(Client) side for the error/failure response being sent.
Check Logs

## Slide 40: Alepo SDM Troubleshooting

## Slide 41: Alepo SDM Troubleshooting
This section describes the major issues related to SDM and steps to troubleshoot them.
The SDM solution includes AUSF, UDM, UDR, HSS.
Troubleshooting the SDM
The operator must troubleshoot the SDM, when any of the following are reported:
  Authentication Issues
  Handover Issues
  Registration/Deregistration Issues
  Configuration Issues

## Slide 42: Authentication Issues

## Slide 43: Authentication Issues
This section describes the two major authentication issues a subscriber might encounter in 4G and 5G networks.
Subscriber authentication not successful (4G)
Subscriber authentication not successful (5G)

## Slide 44: Subscriber authentication not successful (4G)
Possible Causes
Authentication of a subscriber can fail due to multiple causes as given below:
Requested IMSI number is not configured in UDR/ HSS components.
Authentication keys mapped to IMSI are incorrect.
Requested IMSI profile is barred.
Preprocessing
Check if the IWF, UDR and HSS are up and running.
Check if any fault alarm is generated by any of the network functions.
Troubleshooting Procedure
The following section includes troubleshooting steps for various diameter messages and their error codes:
Diameter Error Code 5001
Message: Authentication-Information-Request
Reason: User received request identified by “User-Name” diameter avp is unknown to HSS.
Steps to resolve:
Provision SIM with IMSI coming in request.
Associate subscription to provisioned sim.

## Slide 45: Subscriber authentication not successful (4G)
Diameter Error Code 5003
This Diameter messages and error code can occur due to multiple reasons:
Case 1
Message: Authentication-Information-Request
Reason: User received request identified by “User-Name” diameter avp is barred using operator determined barring parameter in SDM portal.
Steps to resolve:
Search the user present in request in Subscriber Management menu of SDM portal, click on view.
Navigate to Access & Mobility tab on subscriber page, click on ODB Data.
Set ODB Packet Services to None.
Check application logs for above diameter messages for Interworking Function (IWF) & Home Subscriber Server (HSS):
Case 2
Message: Authentication-Information-Request
Reason: Visited PLMN of Subscriber as indicated by “Visited-PLMN-Id” diameter avp is not allowed in the HSS configuration.
Steps to Resolve:
Configure visited PLMN of Subscriber as indicated by “Visited-PLMN-Id” diameter avp in “plmnList” or “allowedPlmns” array parameter under nfInstaces parameter group in configuration of HSS.
Check application logs for above diameter messages for Interworking Function (IWF) & Home Subscriber Server (HSS):

## Slide 46: Subscriber authentication not successful (4G)
Diameter Error Code 5012
Message: Authentication-Information-Request
Reason: Some issue in SIM provisioned for subscriber.
Steps to Resolve:
Check for the SIM in SIM Info section
If the SIM is present, then check for its details as obtained from SIM vendor.
If there is any correction, then update the SIM through a new batch using SIM Batch menu in SIM Batch Management in SDM portal.
Check application logs for above diameter messages for Interworking Function (IWF) & Home Subscriber Server (HSS):

## Slide 47: Subscriber authentication not successful (5G)
Possible Causes
Authentication of the user can fail due to:
Error in core network of Alepo’s components
Error in core network during user authentication
Request not reaching network components.
Serving network issue
Preprocessing
Check if the AUSF, UDM, UDR are up and running.
Check if any fault alarm is generated by any of the network functions.
Troubleshooting Procedure
This section explains how to identify and troubleshoot the problem.
Follow the steps given below to check if the issue exists in core network of Alepo's components (AUSF-UDM-UDR):
Get the approximate timestamp and the user details (either IMSI or SUPI) of the affected user/users.
Begin with AUSF logs and use approximate timestamp and user details to narrow down search.
3. If authentication has failed due to any error in core network components, then AUSF logs has non 2xx error code (200 or 201)

## Slide 48: Subscriber authentication not successful (5G)
Response logs are identified by "Sending Response" string, present at the end of the logwrite line as shown above. If there is any non 2xx status code e.g., 403 as shown above, then this indicates error has occurred in core network side during user authentication.
In case of authentication confirmation (second API in authentication flow in 5G AKA) even if the response code is 200, authentication might not be successful from core network perspective. This is illustrated more in troubleshooting steps.
  If you are unable to find any logs for response even with narrowed down timestamps and user details, then it indicates that the request has not reached components and the issue might be in the serving network side.
HTTP Status Code 200
Message: API - PUT /ue-authentications/{authCtxId}/5g-aka-confirmation
Reason
This is not an error code but, it can indicate the problem if user's authentication is not accepted by AUSF as the response parameter, resStar(RES*) of a user sent by network, does not match with expected response parameter XRESStar(XRES*) stored by AUSF in its local context.
This API is for confirming authentication status. If AUSF does not accept response sent by UE through network, authentication is still marked as failed as indicated by "AUTHENTICATION_FAILURE" in the response body.
Steps to resolve:
Check for the SIM in SIM Info section
If the SIM is present, then check for its details as obtained from SIM vendor.
If there is any correction, then update the SIM through a new batch using SIM Batch menu in SIM Batch Management in SDM portal.

## Slide 49: Subscriber authentication not successful (5G)
HTTP Error Code 400
Message: API: POST /ue-authentications
Reason:
This is a bad request error. It means, either "supiOrSuci" or serving network name, sent in the request body is not acceptable.
supiOrSuci or serving network name is missing.
Step to resolve:
This is a client error. To resolve this issue, contact the serving network vendor/team.
HTTP Error Code 403
Message: API - POST /ue-authentications
Reason: Authentication is rejected due to following reasons:
odbPacketServices parameter in accessMobilitySubscription data in subscriber database is not supported by AUSF. This parameter decides operator determined barring of subscriber.
User's PLMN is not supported by AUSF.
Steps to resolve:
Search for the user using its IMSI in the Subscriber Management on SDM portal, then click on view subscriber.
Check ODB Data section under Access & Mobility Tab. If ODB is set for packet services or for roaming, then unset it.
Subscriber of other PLMN not allowed by AUSF is not authenticated by AUSF. Configure visited PLMN of Subscriber as indicated by serving network name parameter in “plmnList” or “allowedPlmns” array parameter under nfInstaces parameter group in configuration of AUSF.

## Slide 50: Subscriber authentication not successful (5G)
HTTP Error Code 404.
This error message occurs due to multiple reasons:
Case 1
Message API - POST /ue-authentications
Reason: Information presented by client is not available at the server.
This can occur due to a user unknown error or user's authentication subscription might not have been provisioned through SDM portal.
Steps to resolve:
Provision subscriber via SIM Batch Management & Subscriber Management menus in SDM portal.
Case 2
Message: API - PUT /ue-authentications/{authCtxId}/5g-aka-confirmation
Reason: Server is unable to process the request due to following internal reasons:
AUSF Database is down
AUSF is unable to update the authentication status with the help of UDM /UDR.
Steps to resolve:
Contact system administrators to restart the process if database of AUSF or UDR is down. Restart processes for database can vary from environment to environment, depending upon how database is deployed.
Restart the application container /POD (what is pod), if UDM application is down.
These steps can depend upon the environment, in general for kubernetes like environments, new POD will be auto-spawn if the current POD goes down.

## Slide 51: Subscriber authentication not successful (5G)
HTTP Error Code 500
Message: API: POST /ue-authentications
Reason: Error could be due to one of the following reasons:
AUSF/UDM/ UDR database is unreachable / down
UDR's subscriber database is down
UDM is unable to generate proper authentication vectors required for authentication
AUSF is unable to generate keys & hashed values of authentication vectors obtained from UDM
Steps to Resolve
In this case, check if correct values of Ki & Opc are provisioned in subscriber through SIM Batch Management in SDM portal.
If there is any correction, then update the SIM using a new batch through SIM Batch Management menu in SDM Portal.
Contact system administrators to restart the database if AUSF or UDR is down
Restart processes for database varies for each environment depending on how database is deployed. It is out of scope of this document to describe all restart processes. If UDM application is down, then restart the application container / POD. Generally, for Kubernetes like environments, new POD will be auto-spawn if the current POD goes down. If UDM is unable to generate Authentication vectors, it will respond with 500 error code to AUSF

## Slide 52: Handover Issues

## Slide 53: Handover Issues
There are four possible scenarios where subscriber handover can fail:
  Subscriber 4G-4G handover fails
  Subscriber 4G-5G handover fails
  Subscriber 5G-4G handover fails
  Subscriber 5G-5G handover fails

## Slide 54: Subscriber 4G-4G handover fails
Possible Causes
  Handover can fail due to:
  Error in core network components
  Database is down
  UDR is down
  Subscriber database is down
Preprocessing
  Check if the HSS, UDR are up and running
  Check if a fault alarm is generated by any of the network functions
Troubleshooting Procedure
The following section includes troubleshooting steps for various diameter messages and their error codes:
  Diameter Error Code 5001
  Diameter Message: ULR
Reason: Internal server error can occur due to the following reasons:
  HSS/ UDR is down
  Database is down.
  Invalid subscriber data
Steps to Resolve:
  If database is down, restart, depending on type of deployment environment.
  If UDR is down, restart the UDR network function.
  If the deployment of UDR is a POD on Kubernetes, then it restarts automatically.
  If subscriber database has invalid values, then correct the values by re-provisioning same subscriber correctly.

## Slide 55: Subscriber 4G-4G handover fails
Possible Causes
  Handover can fail due to:
  Error in core network components
  Database is down
  UDR is down
  Subscriber database is down
Preprocessing
  Check if the HSS, UDR are up and running
  Check if a fault alarm is generated by any of the network functions
Troubleshooting Procedure
The following section includes troubleshooting steps for various diameter messages and their error codes:
  Diameter Error Code 5001
  Diameter Message: ULR
Reason: Internal server error can occur due to the following reasons:
  HSS/ UDR is down
  Database is down.
  Invalid subscriber data
Steps to Resolve:
  If database is down, restart, depending on type of deployment environment.
  If UDR is down, restart the UDR network function.
  If the deployment of UDR is a POD on Kubernetes, then it restarts automatically.
  If subscriber database has invalid values, then correct the values by re-provisioning same subscriber correctly.

## Slide 56: Subscriber 4G-5G handover fails
Possible Causes
  Handover can fail:
  Due to issue on serving network side
  Due to issue on core network side
  When the subscriber is not allowed to attach into NR RAT Type
Preprocessing
  Check if the HSS, UDM, UDR are up and running
  Check if a fault alarm is generated by any of the network functions
  4G-5G Handover:
  HSS:
  Interworking5G: 1
Troubleshooting Procedure
  The following section includes troubleshooting steps for various API and their error codes:
HTTP Error Code 403
Message: API - AMF Registration PUT
Reason: Radio access type New Radio (NR) is restricted in subscriber profile in database.
Steps to Resolve:
  Search the subscriber coming in request on SDM portal in Subscriber Management menu, click on view subscriber.
  Under Access & Mobility tab in subscriber page, check Access Network section for RAT restrictions configured. If ratType coming in request was not meant to be blocked, then set RAT restrictions to None.

## Slide 57: Subscriber 4G-5G handover fails
Logs of sending response is shown below
HTTP Error Code 404
Message API - AMF Registration PUT
Reason: This is an internal server error, which occurs due to the following reasons:
UDR is down or is unreachable
Database is down or is unreachable
Subscriber data has invalid values in the database, so UDM is unable to complete registration request completely
Steps to resolve:
If Database is down, restart the same. Steps of restart depend upon type of deployment. In case of Kubernetes deployment if database is deployed as a
POD, then it will be automatically restarted after some time.
2. If Subscriber database has invalid values, correct the same by re-provisioning same subscriber correctly.

## Slide 58: Subscriber 5G-4G handover fails
Possible Causes
Handover can fail:
In component side
On network side
In serving side
If the subscriber is not to be subscribed for an interworking scenario
Preprocessing
Check if the UDM, UDR, HSS are up and running
Check if a fault alarm is generated by any of the network functions
5G-4G handover:
UDM:
Interworking4G: 1
Troubleshooting Procedure
The following section includes troubleshooting steps for various diameter messages and their error codes:
Diameter Error Code 5001
Diameter Message: ULR
Reason: Internal Server Error occurs due to:
HSS/ UDR is down
Database is down
Invalid subscriber data

## Slide 59: Subscriber 5G-4G handover fails
Steps to resolve:
If database is down, restart the same, depending upon type of deployment.
If UDR is down, restart the UDR NF
If the deployment of UDR is a POD on Kubernetes, then it automatically restarts.
If subscriber database has invalid values, correct the values by re-provisioning same subscriber correctly.
Diameter Error Code 5003
Diameter Message: ULR
Reason: Diameter Authorization Rejected. This occurs when subscriber is not allowed in EUTRAN Radio type
Step to resolve: Check subscriber provisioning, if subscriber is not allowed in EUTRAN network then, this failure can occur. If subscriber was not meant to be blocked in EUTRAN network, then this can be unset using SDM Portal.

## Slide 60: Subscriber 5G-5G handover fails
Possible Causes
  Handover can fail due to:
  Error in core network components
  Database is down
  UDR is down
  Subscriber database is down
Preprocessing
  Check if the UDM, UDR are up and running
  Check if any fault alarm is generated by any of the network functions
Troubleshooting Procedure
Below section includes troubleshooting steps for various API and their error codes:
HTTP Error Code 404
  Message: API - AMF Registration PUT
  Reason: This an internal server error which can occur due to following reasons:
  Database is down/ unreachable.
  UDR is down / unreachable.
  Subscriber data present inside database has invalid values, so UDM is unable to complete registration request completely.
Steps to Resolve:
  If Database is down, restart the database depending upon type of deployment.
  If subscriber database has invalid values, correct the same by re-provisioning same subscriber correctly.

## Slide 61: Registration/Deregistration Issues
The following are the four possible scenarios:
  Subscriber registration is not successful (4G)
  Subscriber registration is not successful (5G)
  Subscriber De-registration is not successful ( 4G)
  Subscriber Deregistration is not successful (5G)

## Slide 62: Subscriber registration is not successful (4G)
Possible Causes
LTE registration of a subscriber can fail due to the following reasons:
Requested IMSI is not configured in HSS/UDR
Accessing from restricted access network
Requested IMSI profile is barred
Preprocessing
Check if the HSS, UDR are up and running
Check if any fault alarm is generated by any of the network functions
Troubleshooting Procedure
Below section includes troubleshooting steps for Diameter Messages and error codes.
Diameter Error Code 5001
Message: Update-Location-Request
Reason: User received in request identified by “User-Name” diameter avp is unknown to HSS.
Steps to Resolve:
Provision SIM with IMSI coming in request
Associate subscription to provisioned sim
Check Logs in IWF, HSS,

## Slide 63: Subscriber registration is not successful (4G)
Message: Update-Location-Request
Reason: UDR/Database is unreachable
Steps to Resolve: Ensure UDR is up and running
  Check logs of IWF & HSS
Diameter Error Code 5003
Message: Update-Location-Request
Reason: Access from disallowed network. (Access from disallowed network. (Configured HPLMN and requested visted-plmn-id is not matched, then hss response with 5003)
Steps to Resolve: N/A
  Check logs of IWF & HSS
Diameter Error Code 5004
Message: Update-Location-Request
Reason: Received IMSI profile is barred from accessing LTE services
Steps to Resolve: Remove barring from subscription
  Check logs of IWF & HSS

## Slide 64: Subscriber registration is not successful (5G)
Possible Causes
Registration can fail due to:
AMF registration failure
SMF Registration failure
subscriber's data obtained by AMF/SMF is not suitable for AMF to register for access & mobility and SMF to register for PDU Session.
Preprocessing
Check if the HSS, UDR are up and running.
Check if a fault alarm is generated by any of the network functions.
Troubleshooting Procedure
How to identify and troubleshoot the problem
Follow the below steps to ascertain that problem of registration lies with Alepo's components for a given UE:
  Obtain the User's Identifier which is SUPI (in case of 3GPP access) and GPSI (in case of non-3gpp access).
  Obtain approximate timestamp when user was authenticated or switched-on device.
  Registration call flows occurs after authentication procedure. Once the exact logs are narrowed down, find out the errors in "Sending Response" logs for below APIs:
AMF Registration failure for API resource: /SUPI/registrations/amf-3gpp-access
SMF Registration failure for API resource: /ueId/registrations/smf-registrations
Subscription (to receive notification on data change) failure:

## Slide 65: Subscriber registration is not successful (5G)
The following section includes troubleshooting steps for various API and their error codes:
HTTP Error Code 403
Message API: AMF Registration PUT
Reason: This error occurs when:
Radio Access type of subscriber for registered AMF is restricted in the subscriber profile in database
Subscriber is not authenticated in the serving network of AMF
Indicated by GUAMI value in request
Steps to resolve:
Search the subscriber coming in request on SDM portal in Subscriber Management menu, click on view subscriber.
Under Access & Mobility tab in subscriber page, check Access Network section for RAT restrictions configured. If ratType coming in request was not meant to be blocked, then set RAT restrictions to None.
Authenticate the subscriber if the subscriber is not authenticated from the serving network of the AMF.
Cross-check MCC & MNC present in GUAMI of request with servingNetworkName in authenticationStatus in subscriberprofile in database and check if they match. This is done to check from which PLMN or serving network the subscriber was authenticated.
If they do not match, UDM sends error & logs of sending response

## Slide 66: Subscriber registration is not successful (5G)
HTTP Error Code 400
This error code can occur due to multiple reasons as given by different case numbers:
Case 1
Message API: AMF Registration PUT
Reason: This error comes when request is badly formed when:
Mandatory parameter like amfInstanceId, deregCallbackUri,deregCallbackUri, ratType are missing in the request
Parameters are present but, have invalid values that are not recognized by server
Steps to resolve:
This error must be checked from AMF since, it has sent a malformed request.
Logs of sending response from the UDM side
Case 2
Message API: AMF Registration PATCH
Reason: This error occurs when PATCH operation is used to modify AMF Registration data fields which are not allowed to be modified e.g, amfInstanceId, PLMN of GUAMI etc.
Steps to resolve:
This is a client error. Check the configuration from AMF if different values of parameters that are not allowed to be modified are sent.
If a totally different AMF is sending PATCH request to modify registration, this is clearly an error. Logs of "Sending Response"

## Slide 67: Subscriber registration is not successful (5G)
Case 3
Message: API - AMF Registration PATCH
Reason: This error occurs when PATCH operation is sent with a request body missing any mandatory parameters such as GUAMI.
Steps to resolve:
This is a client-side error. It must be checked why AMF is not including all parameters for registration.
Check Logs of error messages
Case 4
Message: API - SMF Registration PUT
Reason:
This error occurs when mandatory parameters are missing in the request such as: smfInstanceId,pduSessionId,singleNssai,plmnId
This can occur when there is a mismatch in pdusession ID sent by SMF in the body and in the URI.
Steps to resolve:
This is a client-side error and must be checked by them.
Check Logs of error messages

## Slide 68: Subscriber registration is not successful (5G)
Case 5
Message: API - SDM Subscription POST
Reason: This error can occur when request is sent:
Without mandatory parameters
With invalid parameters
With both amfServicename and singleNssai or dnn parameters present in request.
Steps to resolve:
Since this is a client error, it must be checked by SMF to determine why such a request is sent/ triggered.
Check Logs of "Sending Response"
Case 6
Message: API - SDM Data get Multiple datasets
Reason:
This error occurs when the get request sent by AMF / SMF is malformed.
Example: Invalid query parameters or invalid number of query parameters (at least 2 parameters must be there)
Steps to resolve:
This is a client-side error. Please check AMF / SMF configuration so that it sends the correct requests.
Check Logs of "Sending Response"

## Slide 69: Subscriber registration is not successful (5G)
HTTP Error Code 404
This error code can occur due to multiple reasons as given by different case numbers:
Case 1
Message: API - AMF Registration PUT
Reason: This is an internal server error which occurs when:
Database is down/ unreachable
UDR is down / unreachable
Invalid values are present in subscriber database, so UDM is unable to complete registration request entirely.
Steps to resolve:
If Database is down, restart the process, depending on type of deployment.
If Subscriber database has invalid values, correct it by re-provisioning the same subscriber.
Case 2
Message: API - AMF Registration PUT
Reason: This error occurs in two scenarios:
When the user does not exist in the subscriber database
User exists but, does not have PLMN subscription associated with it.
Steps to resolve:
Check if the user exists in the database.
If the user is non-existent, then user needs to be added in the system through provisioning. Check Logs of "Sending Response“
3. If user exists in the database but PLMNGroup associated with user does not exists, then PLMN group subscription needs to be added from SDM Portal Subscriber Management tab.
4. Check Logs of "Sending Response“
Notes: Can be added as one of the failure case – API AMF Registration PUT
- In the AMF registartion case udm responses (HTTP Error code 404) with message "No authentication status data for given subscriber-id in database", then requires to check whether Authentication is successfully done or not.

## Slide 70: Subscriber registration is not successful (5G)
Case 3:
Message: API - AMF Registration PUT
Reason: No authentication status data for given subscriber-id in database
Steps to resolve:
In the AMF registration case udm responses (HTTP Error code 404) with message "No authentication status data for given subscriber-id in database", then requires to check whether Authentication is successfully done or not.
Notes: Can be added as one of the failure case – API AMF Registration PUT
- In the AMF registration case udm responses (HTTP Error code 404) with message "No authentication status data for given subscriber-id in database", then requires to check whether Authentication is successfully done or not.

## Slide 71: Subscriber registration is not successful (5G)
Case 4
Message: API - AMF Registration PATCH
Reason: This error occurs when PATCH operation is used to modify AMF Registration which does not exist in database.
Steps to resolve:
This is a client error. It must be checked why AMF is trying to send PATCH request before completing the registration. Check Logs of "Sending Response"
Case 5
Message API - AMF Registration PATCH
Reason: This is an internal server error in completing request processing which can occur when UDR is down, or database is down.
Steps to resolve:
If database is down, restart the same
Restart steps vary from environment to environment. For example, kubernetes, VM based deployment etc.
If UDR is down, restart the application container
If it is a Kubernetes environment, then it gets auto restarted
Case 6
Message: API - SMF Registration PUT
Reason:
This error can occur when:
User is not present in database
User is present but not subscribed to slice / dnn which is sent by SMF in request
Steps to resolve:
Check if the user exists in the system, if it does not exist, then provision the user correctly.
If the user is not subscribed to slice / dnn which is sent by SMF in request, then check, why user is not subscribed & a subscription can be added to given slice or dnn via user's PLMN group if necessary.
Check Log of "Sending Response"

## Slide 72: Subscriber registration is not successful (5G)
Case 7
Message: API: SDM Subscription POST
Reason: This error can occur when Request is sent by AMF which is not registered for 3gpp access.
Steps to resolve:
AMF's SDM subscription is not allowed unless AMF registers for access.
This must be checked from client side. If this is the error, check logwrites of "Sending Response"
Case 8
Message: API: SDM Data get Multiple datasets
Reason: This error occurs when:
Subscriber does not exist in database
Subscriber exists but the corresponding PLMN data does not exist in database.
Steps to resolve:
To resolve this, subscriber or their PLMN Group provisioning needs to be checked for correctness.
If this is the error, then check log of "Sending Response"
Case 9
Message: API: SDM Data get Multiple datasets
Reason: This error occurs when server is unable to process the request it can occur if:
UDR is down
Database is down
Steps to resolve:
In both cases UDR / Database needs to be restarted. The exact steps will depend on environment. If this is a Kubernetes environment, then it can auto-restart application pods.
If this is the error, check logwrites of "Sending Response"

## Slide 73: Subscriber registration is not successful (5G)
Case 10
Message: API: SDM Data get AM data
Reason: This error occurs when:
Subscriber does not exist in database
Subscriber exists but, their PLMN data does not exist in database
Steps to resolve:
In this case Subscriber or their PLMN needs to be correctly provisioned into the system.
If this is the error, then check log of "Sending Response"
Case 11
Message: API: SDM Data get SM data
Reason: This error occurs when:
Subscriber does not exist in database
Subscriber exists but their PLMN data does not exist in database
Steps to resolve:
In this case Subscriber or their PLMN needs to be correctly provisioned into the system.
2. If this is the error, then check log of "Sending Response"

## Slide 74: Subscriber registration is not successful (5G)
Case 12
Message: API: SDM Data get SMF-Select data
Reason: This error occurs when:
Subscriber does not exist in database
Subscriber exists but their PLMN data does not exist in database
Steps to resolve:
In this case Subscriber or their PLMN needs to be correctly provisioned into the system.
If this is the error, then check log of "Sending Response"
Case 13
Message: API: SDM Data get UE context in SMF Data
Reason: This error occurs when no SMF Registration exists for a subscriber in database.
Steps to resolve:
SMF registration must occur first to create this data in UDR Database.
If this is the error, then check log of "Sending Response"

## Slide 75: Subscriber registration is not successful (5G)
Case 14
Message: API: SDM Data get UE context in SMF Data
Reason: This error occurs when server is unable to process the request it can occur if:
UDR is down
Database is down
Steps to resolve:
  In both cases, UDR and Database must be restarted. The exact steps will depend on the environment. If this is a Kubernetes environment, then it can auto-restart application pods.
  If this is the error, then check log of "Sending Response"

## Slide 76: Subscriber registration is not successful (5G)
Case 15
Message: API: SDM Data get UE context in SMF Data
Reason: This error occurs when server is unable to process the request it can occur if:
UDR is down
Database is down
Steps to resolve:
  In both cases, UDR and Database must be restarted. The exact steps will depend on the environment. If this is a Kubernetes environment, then it can auto-restart application pods.
  If this is the error, then check log of "Sending Response"

## Slide 77: Subscriber De-registration is not successful(4G)
Possible Causes
LTE de-registration of a subscriber can fail due to the following reasons:
Requested IMSI is not configured in HSS/ UDR
UDR/Database is not reachable
Preprocessing
Check if the HSS, UDR are up and running
Check if a fault alarm is generated by any of the network functions
Troubleshooting Procedure
Below section includes troubleshooting steps for Diameter error codes.
Diameter Error Code 5001
Diameter Message: Purge-UE-Request
Reason: Received unknown IMSI
Steps to Resolve: Provision request to be sent to IMSI in UDR
  Check logs of IWF & HSS

## Slide 78: Subscriber De-registration is not successful(4G)
Diameter Message: Purge-UE-Request
Reason: Received UDR/Database is unreachable
Steps to Resolve: Check if UDR is up and running
Check Logs of IWF & HSS

## Slide 79: Subscriber De-registration is not successful(5G)
Possible Causes
Deregistration fails due to the following reasons:
Database is down
UDR is down
Subscriber database is down
When the deregistering AMF is not registered
When the deregistering SMF is not registered
Preprocessing
Check if the UDR, UDM are up and running.
Check if a fault alarm is generated by any of the network functions.
Troubleshooting Procedure
Follow the given steps to find the exact issue on the component side:
Get approximate time stamp & user details
Narrow down the search to the exact de-registration request logwrites & the response given by UDM.

## Slide 80: Subscriber De-registration is not successful(5G)
HTTP Error Code 404
Message API: AMF Deregistration PATCH
Reason: This error comes when deregistering AMF is not registered with Alepo.
Steps to Resolve
This is a client error, an AMF which is not registered must not send de-registration request.
If this is the error, then check log of "Sending Response“
Message: API: AMF Deregistration PATCH
Reason: This error occurs when:
Database is down
UDR is down
Steps to resolve:
Restart database / UDR application
If Kubernetes is the environment, then it can auto-restart application pods.

## Slide 81: Subscriber De-registration is not successful(5G)
Message: API: SMF Deregistration DELETE
Reason: This error comes when deregistering SMF is not registered with Alepo.
Steps to resolve:
This is a client error, an SMF which is not registered must not send de-registration request.
Message: API: SMF Deregistration DELETE
Reason: This error comes when:
Database is down
UDR is down
Steps to resolve:
Restart database / UDR application.
Exact steps to do so will depend upon your environment.
If Kubernetes is the environment, then it can auto-restart application pods.

## Slide 82: Configuration Issues

## Slide 83: Configuration Issues
Given below are the Configuration Issues
  Unable to associate 4G/5G subscription to SIM
  Unable to create/update template/group
  Unable to view/list templates/groups
  Unable to import SIM batch
  Unable to view 4G/5G online context
  Unable to associate AM/SM policy to subscription

## Slide 84: Unable to associate 4G/5G subscription to SIM
Possible Causes
Association of 4G/5G subscription can fail due to multiple reasons:
SIM profile is marked in Used state
PLMN group is mandatory during subscription association
Slice template association is mandatory during subscription association
Back-end API server or database is unreachable
Preprocessing
Check if the SDM Portal’s frontend and backend are up and running.
Troubleshooting Procedure
Below section includes troubleshooting steps for various API and their error codes.
HTTP Error Code 400
Message API/User Interface: Associate 4G subscription (API operation: PUT)
Reason: SIM profile status is Used
Steps to resolve:
Ensure SIM profile status is available.
Message API/User Interface: Associate 5G subscription (API operation: PUT)
Reason: PLMN group is not passed as provisioning parameter
Steps to resolve:
If any SIM is subscribed to 4G or 5G subscription, PLMN group is mandatory for associating templates.

## Slide 85: Unable to associate 4G/5G subscription to SIM
HTTP Error Code 500
Message API/User Interface: Associate 4G subscription (API operation: PUT)
Reason:
Database is unreachable or has an internal error
Back-end API server is not reachable
Steps to resolve:
Ensure database & back-end API servers are up and running.
Message API/User Interface: Associate 5G subscription (API operation: PUT)
Reason:
Database is unreachable or internal error
Back-end API server is not reachable
Steps to resolve:
Ensure database & back-end API server are up and running.

## Slide 86: Unable to create/update template/group
Possible Causes
Addition or update of any template or group can fail for the following reasons:
due to duplicate values of name or any other unique parameter
E.g., Addition of a PLMN template with duplicate combination of mcc & mnc.
adding or updating any parameter with incorrect data type.
back-end API server or database is unreachable at the time of operation.
Preprocessing
Check if the SDM Portal’s frontend and backend are up and running.
Troubleshooting Procedure
Below section includes troubleshooting steps for various API and their error codes.
HTTP Error Code 400
Message: API/User Interface: Adding/Updating Slice template (API operation: POST/PUT)
Reason:
Duplicate slice template name
Duplicate combination of SST & SD
Incorrect data type for any input parameter

## Slide 87: Unable to create/update template/group
Steps to resolve:
Before adding or updating, ensure the following steps are considered:
Slice template name shall be unique
Combination of SST & SD is unique across all slice templates
Data type of all input parameters must be as per API guide
Message: API/User Interface: Adding/Updating PLMN template (API operation: POST/PUT)
Reason:
Duplicate PLMN template name
Duplicate combination of MCC & MNC
More than one HPLMN template
Incorrect data type for any input parameter
Steps to resolve:
Before adding or updating, ensure the following steps are considered:
PLMN template name shall be unique
Combination of MCC & MNC is unique across all PLMN templates
Data type of all input parameters must be as per API guide

## Slide 88: Unable to create/update template/group
Message: API/User Interface: Adding/Updating DNN template (API operation: POST/PUT)
Reason:
Duplicate DNN template name
Incorrect data type for any input parameter
More than one wild card DNN
Steps to Resolve:
Before adding or updating, ensure the following steps are considered:
DNN template name must be unique
Data type of all input parameters must be as per API guide
Message: API/User Interface: Adding/Updating Usage Limit (API operation: POST/PUT)
Reason:
Duplicate usage limit or limit ID
Incorrect data type for any input parameter
Steps to Resolve:
Before adding or updating, ensure the following steps are considered:
Usage limit & LimitId must be unique
Data type of all input parameters must be as per API guide

## Slide 89: Unable to create/update template/group
Message: API/User Interface: Adding/Updating Location group (API operation: POST/PUT)
Reason:
Duplicate location group
Incorrect data type for any input parameter
Steps to Resolve:
Consider the following steps before adding or updating:
Location group name must be unique
Data type of all input parameters must be as per API guide
Message: API/User Interface: Adding/Updating Presence Info template (API operation: POST/PUT)
Reason:
Duplicate presence info template
Incorrect data type for any input parameter
Steps to Resolve:
Before adding or updating, ensure the following steps are considered:
Presence info template name must be unique
Data type of all input parameters must be as per API guide.

## Slide 90: Unable to view/list templates/groups
Possible Causes
Listing or viewing template or group can fail due to the following reasons:
No templates or groups are present in the system
Back-end API server or database is unreachable at the time of operation
Preprocessing
Check if the SDM Portal’s frontend and backend are up and running.
Troubleshooting Procedure
Below section includes troubleshooting steps for various API and their error codes.
Use the below table for troubleshooting for various error codes:
HTTP Error Code 400
Message: API/User Interface: Get All PLMN/Slice/DNN templates (API operation: GET)
Reason: No templates or groups in the system.
Steps to resolve: Ensure relevant template or group is configured in the system.
Message: API/User Interface: Fetch an individual PLMN/Slice/DNN templates (API operation: GET)
Reason: Relevant template or group are not present in the system
Steps to resolve: Before querying for template/group by id, check its presence using Get All API.
HTTP Error Code 500
Message API/User Interface: Get All PLMN/Slice/DNN templates (API operation: GET)
Reason: Back-end API server or database is not reachable.
Steps to resolve: Ensure API server or database is connected.

## Slide 91: Unable to import SIM batch
Possible Causes
Batch SIM import can fail due to the following reasons:
uploaded batch file has invalid file extension i.e., other than .csv
incorrect data format of batch file (Not as per template)
batch processor micro-service or database is unreachable.
Preprocessing
Check if an SDM Portal frontend is up and running.
Check if an SDM Portal backend is up and running.
Troubleshooting Procedure
Use below table for troubleshooting for various errors.
Error: File not uploaded
API/User Interface: Import SIM Batch
Reason: File extension
Steps to resolve: Ensure batch file has extension as ".csv"

## Slide 92: Unable to import SIM batch
API/User Interface: Import SIM Batch
Error: File is not uploaded
Reason:
Batch processor back-end service is down
Database is not reachable
Steps to resolve: Batch processor back-end service & database must be restarted and made available.

## Slide 93: Unable to view 4G/5G online context
Possible Causes
Viewing of 4G/5G subscription online context can fail due to the following reasons:
No 4G/5G context is available
Back-end context-data API server or database is not reachable
Preprocessing
Check if the SDM Portal’s frontend and backend are up and running.
Troubleshooting Procedure
Below section includes troubleshooting steps for various API and their error codes.
HTTP Error Code 400
Message: API/User Interface: View 4G/5G context (API operation: GET)
e.g. Fetch AMF Context by SUPI API (5G)
Fetch LTE Context by SUPI (4G)
Reason:
4G or 5G online context is not available
Steps to resolve: Ensure 4G or 5G online context is available for subscriber i.e., Register UE with 4G or 5G network.

## Slide 94: Unable to view 4G/5G online context
HTTP Error Code 500
Message: API/User Interface: View 4G/5G context (API operation: GET)
Reason:
Database is unreachable or internal error
Back-end context-data API server is not reachable
Steps to resolve:
Make sure database & back-end API server is up and running.

## Slide 95: Unable to associate AM/SM policy to subscription
Possible Causes
Association of AM/SM Policy association to subscription fails if:
slice group is not present in the system (Mandatory for SM policy association)
back-end API server or database is unreachable
Preprocessing
Check if the SDM Portal’s frontend and backend are up and running.
Troubleshooting Procedure
Below section includes troubleshooting steps for various error codes.
HTTP Error Code 400
Message: API/User Interface: Associate SM Policy for Subscription by SUPI API (API operation: PUT)
Reason: Slice group is not passed as provisioning parameter.
Steps to resolve:
Slice group must be configured and is mandatory for associating SM policy.

## Slide 96: Unable to associate AM/SM policy to subscription
HTTP Error Code 500
Message API/User Interface: Associate AM Policy for Subscription by SUPI API (API operation: PUT)
Reason:
Database is not reachable or has an internal error
Back-end API server is not reachable
Steps to resolve: Ensure database & back-end API server both are up and running.
Message: API/User Interface: Associate SM Policy for Subscription by SUPI API (API operation: PUT)
Reason:
Database is unreachable or has an internal error
Back-end API server is not reachable
Steps to resolve:
Ensure database & back-end API server both are up and running.

## Slide 97
Corporate HQ
Austin, TX, USA
sales@alepo.com
Follow Us
www.alepo.com
AlepoUSA
@AlepoUSA
Company/Alepo